## Slide 1
Recovery of lost map for monocular simultaneous localization and mapping
Data：2019.10.14
Respondent：Ruyu Liu
Notes: Before the presentation, please allow me to explain. I am not the contestant in this competition; for some reason, the contestant cannot be here, so that I will do this report for them. Unfortunately，I cannot answer any questions about the details of the project.
Today, I am going to talk about the recovery of the lost map for monocular simultaneous localization and mapping.

## Slide 2
PURPOSE
PART TWO
Notes: So, What is our purpose?

## Slide 3
Map recovery by means of IMU
Map coordinate system conversion
Fast searching and Map point matching strategy
Error correction
Joint optimization
Research difficulties
Problem
Solution
Tracking Lost
Notes: SLAM technology can be applied in many fields, such as automatic driving, virtual reality, robots.However, in the real environment, the motion is involved, such as moving too fast, high or low brightness, weak environment, and so on, which will lead to visual SLAM failure.Relocation is the common solution of track lost. The condition of relocation is that: the device must go back to the old environment, or the current environment is similar to the old one.Based on this problem, a map recovery and fusion algorithm using IMU are proposed to solve the problem of track lost. The algorithm is based on the ORB SLAM framework. Once the track lost, even if the relocation cannot be work, our method can still track and map. Our approach has a weak dependence on the environment. After the initialization succeed, the map information before the relocation can be saved.
SLAM技术可应用于许多领域，如自动驾驶、增强和虚拟现实、移动机器人.然而现实生活中的运动往往比较复杂， 例如相机运动过快时产生的图像运动模糊、以及在高亮或低亮、环境纹理特征较弱等情况下都会导致视觉SLAM跟踪失败.目前采用最多的解决跟踪失败的方案是重定位。重定位需要：设备必须回到之前能跟踪上的场景中系统才能继续跟踪建图；或者要求当前场景与地图具有较高的相似性。
针对此问题，提出了一种基于IMU 的地图恢复融合算法解决跟踪失败问题。算法基于单目ORB_SLAM的框架，在系统跟踪失败后，即使无法满足重定位要求，也能继续进行跟踪建图。该方法对场景的依赖较弱，只要初始化成功，就能保存重定位之前的地图信息。

## Slide 4
METHOD
Notes: Next, I will introduce the details of our solution.

## Slide 5
Algorithm framework
The ORB_SLAM framework is used as the basic framework of the map fusion algorithm and modified on the basis of it.
Tracking
After relocation, do not relocate, re-initialize, create a new map, and save the created map before the loss
Loop Closing
Word bag model (proposed an improved matching strategy)
Local Mapping
Scale estimation algorithm
Map Fusion
Image
Initialization
Pose estimation
Scale estimation
Mapping optimization
Initialization
Pose estimation
Scale estimation
Mapping optimization
Joint optimization
Loop closure
IMU
Map coordinate system conversion
Loop closure
Last Map
Lost
Map point matching
Error correction
Current Map
Map Fusion
IMU
Established a link between two keyframes and map points before and after
Notes: Our method is based on the ORB SLAM framework. As shown in figure, the framework of original ORBSLAM can be divided into three parts, tracking, mapping, and loop closing. In our method, the tracker will not relocate after tracking lost, but reinitialize, create a second map, and save the lost map at the same time. The scale estimation algorithm is added to local mapping. Besides, we add a new thread, which is Map fusion. In map fusion, we first estimate the scale, translate the old coordinate system to the current coordinate system based on IMU estimation. However, there are errors in transformation because of the IMU noise. So, we propose an error correction method to optimize the translation.Firstly, we find matching points between the two maps. Next, estimate the motion between matching points. Then, map fusion, the keyframe, and the map points infusion map will be used in subsequent tracking and mapping.
由于ORB_SLAM算法框架比较完善，具有极高的精度和鲁棒性，因此将ORB_SLAM框架作为地图融合算法的基本框架并在其基础上进行修改，算法框架如图所示。ORB_SLAM的算法框架可分为3个线程，分别为跟踪、局部建图和回环检测，本文算法将跟踪线程改为丢失后不进行重定位，而是重新进行初始化，新建第2个地图，同时保存丢失前的已建好的地图，在局部建图线程中加入尺度估计算法。此外，还增加了一个新的线程进行地图融的过程。在这个新的线程中，我们首先进行尺度估计，将前一个地图坐标系通过IMU计算得到的转换关系转换到当前地图的坐标系中。然而直接转换存在误差（是因为IMU测量数据存在噪声）。所以我们需要优化这一转换关系。提出一种误差修正方法，先寻找两个地图之间的匹配点。再计算匹配点之间的运动估计，然后进行地图融合。地图融合结束后，后续的跟踪建图中将会同时使用两个地图的关键帧和地图点信息进行优化。

## Slide 6
Map coordinate system conversion
Map before the loss
New map
World Coordinate System
Camera Coordinate System
World Coordinate System
Camera Coordinate System
IMU
Notes: In the monocular SLAM, the motion trajectory and map is unknown scale because of the depth information is unknown.
Therefore, there is a scale difference between each initial map. The scale must be unified before map fusion. We use the scale estimation method provided by VI ORBSLAM to estimate the real scale between the two maps.
Besides, when tracking lost, the map created by reinitialized is different from the old map. As shown in the figure, we use IMU to estimate the camera pose during the track lost, and obtain the transformation relationship between the old map and current map can be estimated. Then, we unify the two map.
单目SLAM系统中,由于深度信息未知，无法得到运动轨迹以及地图的真实大小，生成的地图的尺度是任意的。因此，每次初始化后的地图之间存在一个尺度差异，进行地图融合之前首先必须统一尺度。我们使用VI orbslam中提供的尺度估计方法估计两个地图的真实尺度。
此外，当视觉跟踪失败，系统重新初始化创建的地图与丢失前创建的地图的坐标系不同。如图所示，需要得到丢失前最后一帧坐标系和新地图第一帧坐标系之间的转换关系。我们使用IMU传感器获取这一转换关系。通过IMU估计视觉跟踪失败的时间段内的相机位姿，可以将两个坐标系不同的地图转换到同一坐标系下。

## Slide 7
Map point matching strategy
Reference map i-frame key frame Enter the i-frame keyframe of the map M: Match the number of map points in two frames
Situation 1:
Situation 2:
Situation 3:
10 associated keyframes
10 associated keyframes
10 associated keyframes
Notes: There is noise in IMU data and errors accumulated during the integration.
To solve this problem, we design an error correction method which estimates the motion between the two maps by nonlinear optimization.
The primary requirement of estimating motion between maps is seeking the matching 3d points. The traditional method is to traverse all keyframes in two maps, which is time-consuming. Therefore, based on the common view relationship between keyframes, we propose a matching strategy, which is divided into 3 cases.
Case1, map point matching is performed on the last frame keyframe Xn in the old mapand the first frame keyframe Y1 in a new map. Because these two frames are closest in time, so they are close in space and are likely to match. If the number of matching map points is less than 5, Xn will skip the first ten frames with the largest point of view with Y1 and match the next keyframe. After traversing all the keyframes in the new map, if the number of map points matched successfully is less than 5, then match frame X(n-10). The reason is that the frames close to Xn are similar if y1 cannot match Xn; it also cannot match the frame close to Xn.
Case2, If the number of matched map points between the Xn and Y_1 is more than 20, then Xn match to the first ten frames of Y1 with a total view. To reduce the repeated match, the one with the most matching map points is selected. Then, re-match keyframes in the new map from X(n−10)
Case3, if the number of matched map points is between 5 to 20, Xn continue to match the Y2 until the case 2 is met or the keyframe in the new map is traversed, then match X_(n−1) and keyframes in the new map.
虽然通过IMU和视觉结合可以估计出陀螺仪和加速度的偏差，但是IMU的测量数据仍然存在噪声，特别是求解位移需要对加速度进行两次积分，进一步累计了误差，导致地图融合产生较大的偏差。为解决这个问题，提出一种误差修正的方法，通过非线性优化求解两个地图点之间的运动估计。求解两个地图点的运动估计，首先需要得到两个地图中一组匹配的3维点。为了找到这样的一组匹配点，传统的做法是遍历两个地图所有的关键帧，比较耗时。因此本文基于关键帧之间的共视关系，提出了一种改进的匹配策略，共分3种情况分别考虑：
情况1），将丢失前的地图中的最后1帧关键帧和新地图的第1帧关键帧进行地图点匹配, 因为对两个地图来说，这两帧在时间上是最接近的，那么空间上相对也比较接近，能够匹配的可能性比较大。若匹配成功的地图点数量小于5，那么直接跳过与共视点最多的前10帧，而与接下来的关键帧进行匹配, 若遍历完新地图中所有的关键帧后，若匹配成功的地图点数都小于5，那么接下来就对进行匹配。直接跳至是因为，与相邻的几帧都与其具有极高的相似性，若与匹配上的概率很低，那么与其相邻几帧的匹配概率也相对较低。
情况2），若和匹配上的地图点数量大于20, 那么对和共视点最多的前10帧进行匹配，为减少重复匹配，选取其中匹配成功的地图点数量最多的那一帧，完成后重新从开始对新地图中的关键帧进行匹配。
情况3），若与配上的地图点数在5和20之间，那么继续与行匹配，直到符合情况2或者对新地图中的关键帧都遍历结束，对和新地图中的关键帧进行匹配。
虽然通过IMU和视觉结合可以估计出陀螺仪和加速度的偏差，但是IMU的测量数据仍然存在噪声，特别是求解位移需要对加速度进行两次积分，进一步累计了误差，导致地图融合产生较大的偏差。为解决这个问题，提出一种误差修正的方法，通过非线性优化求解两个地图点之间的运动估计。求解两个地图点的运动估计，首先需要得到两个地图中一组匹配的3维点。为了找到这样的一组匹配点，传统的做法是遍历两个地图所有的关键帧，比较耗时。因此本文基于关键帧之间的共视关系，提出了一种改进的匹配策略，共分3种情况分别考虑：
情况1），将丢失前的地图中的最后1帧关键帧𝑋_𝑛和新地图的第1帧关键帧𝑌_1进行地图点匹配, 因为对两个地图来说，这两帧在时间上是最接近的，那么空间上相对也比较接近，能够匹配的可能性比较大。若匹配成功的地图点数量小于5，那么𝑋_𝑛直接跳过与𝑌_1共视点最多的前10帧，而与接下来的关键帧进行匹配, 若遍历完新地图中所有的关键帧后，若匹配成功的地图点数都小于5，那么接下来就对X_(n−10)进行匹配。直接跳至𝑋_(𝑛−10)是因为，与𝑋_𝑛相邻的几帧都与其具有极高的相似性，若与𝑋_𝑛匹配上的概率很低，那么与其相邻几帧的匹配概率也相对较低。
情况2），若𝑋_𝑛和𝑌_1匹配上的地图点数量大于20, 那么对𝑋_𝑛和𝑌_1共视点最多Y_1的前10帧进行匹配，为减少重复匹配，选取其中匹配成功的地图点数量最多的那一帧，完成后重新从𝑋_(𝑛−10)开始对新地图中的关键帧进行匹配。
情况3），若𝑋_𝑛与𝑌_1配上的地图点数在5和20之间，那么继续与𝑌_2行匹配，直到符合情况2或者对新地图中的关键帧都遍历结束，对X_(n−1)和新地图中的关键帧进行匹配。
通过这种跳跃式的遍历方式能有效减少匹配的时间。搜索匹配不同大小的两个地图的时间如表1所示，基本稳定在0.08 s左右，满足系统实时的需要，而传统的方法搜索同样数量的关键帧则需要0.2 s左右，时间缩短了2.5倍。

## Slide 8
data set | Lost before map size(KFs) | New map size(KFs) | Modified match time(/s) | Fusion time(/s)
V1_01_easy | 95 | 47 | 0.083 | 0.187
V2_01_easy | 67 | 42 | 0.079 | 0.185
MH_01_easy | 69 | 49 | 0.077 | 0.178
V2_02_medium | 110 | 52 | 0.088 | 0.189
Map point matching strategy
The time of map fusion and matching
Notes: This skipping traversal method can effectively reduce the matching time. The time for searching and matching two maps of different sizes is shown in the table, which is stable at around 0.08 seconds, which satisfies the real-time needs of the system. The traditional method of searching for the same number of keyframes takes about 0.2 seconds, and the time is shortened by 2.5 times.
通过这种跳跃式的遍历方式能有效减少匹配的时间。搜索匹配不同大小的两个地图的时间如表所示，基本稳定在0.08 s左右，满足系统实时的需要，而传统的方法搜索同样数量的关键帧则需要0.2 s左右，时间缩短了2.5倍。

## Slide 9
Error correction
the motion estimation results between the two sets of three-dimensional points are obtained by iterative optimization
the old map is transformed accordingly to compensate for the error of the IMU measurement.
Notes: After obtaining a set of matching map points, the nonlinear optimization is used to solve the motion estimation between the two 3-dimensional points. The two sets of points containing n 3-dimensional points are respectively recorded as P and P^', and the conversion relationship between the two sets of 3-dimensional points is R, t. Then construct an optimization function. The motion estimation results between the two sets of three-dimensional points are obtained by iterative optimization, and then the old map is transformed accordingly to compensate for the error of the IMU measurement.
Only two map coordinate systems are unified, which cannot fuse the two maps because the keyframes and map points of the two maps are not related to each other. We associate the keyframes in the new map with the map points in the old map. Replace the map point of the newly created map with the map point of the lost map, and correspondingly, the keyframe associated with the new map point in the matching point in the original new map will be associated with the old map point in the matching point, thus achieving the purpose of map fusion.
得到一组匹配的地图点后，利用非线性优化求解两组3维点之间的运动估计。将都包含n个3维点的两组点集分别记为和，这两组3维点之间的转换关系为，为三维旋转群 ，那么构造优化函数。通过迭代优化求解得到两组三维点之间的运动估计结果，接着对旧地图进行相应的变换, 从而弥补IMU测量的误差。
仅将两个地图坐标系统一并不能真正将两个地图融合在一起，两个地图的关键帧和地图点并没有相互联系。我们将新地图中的关键帧和旧地图中的地图点关联。用丢失前地图的地图点替代新建地图的地图点，相应的，原本新地图中与这些匹配点中的新地图点关联的关键帧将转换成与匹配点中旧地图点关联，从而达到了地图融合的目的。
得到一组匹配的地图点后，利用非线性优化求解两组3维点之间的运动估计。将都包含n个3维点的两组点集分别记为𝑷和𝑷^‘，这两组3维点之间的转换关系为𝑹∈(𝟑)，𝒕∈ℝ^𝟑，𝑺𝑶(𝟑)为三维旋转群 ，那么构造优化函数。通过迭代优化求解得到两组三维点之间的运动估计结果，接着对旧地图进行相应的变换, 从而弥补IMU测量的误差。

## Slide 10
Joint optimization
After the map fusion is completed, the subsequent tracking and mapping will be optimized using the key frames and map point information of the two maps at the same time.
in local mapping
in loop closing
Notes: After the map fusion is completed, the subsequent tracking and mapping will add the keyframes and map points of the old map to the factor map of the new map for local and global optimization.
地图融合结束后，后续的跟踪建图我们把旧地图的关键帧和地图点加入到新地图的因子图中进行局部和全局的优化。

## Slide 11
RESULT
Notes: Finally, We will evaluate the effectiveness of the method in the following aspects: map accuracy and map integrity
我们从以下几个方面评估方法的效果。即：
地图精确性
地图完整性

## Slide 12
Map accuracy analysis
(b) Original result
(a) Map fusion result
Sequence V1_01_easy comparison result graph
Notes: This is a comparison of the results of the map fusion and the original results. The original result is the result of normal operation, where orb slam is not orb slam does not lose tracking. We make the tracking lost artificially in the left image, then the system re-initializes and performs the map fusion method for fusion. The yellow part is the map point created before the visual tracking failure, and the red and black parts are the map points created by the system after re-initialization after the tracking failure. Purple is the keyframe in the map created before the system is lost, and blue is the keyframe in the new map created after the system is reinitialized. Through the observation of the results, the merged map has little difference from the original un-missed results.
这是地图融合结果和原始结果的对比结果。原始结果是正常运行的结果，其中orbslam是没有跟踪丢失。我们在左边图中人为使得跟踪丢失，然后系统重新初始化，执行地图融合方法进行融合。其中黄色部分为视觉跟踪失败前创建的地图点，红色和黑色部分是系统在跟踪失败后重新初始化后创建的地图点。紫色为系统丢失前创建的地图中的关键帧，蓝色为系统重新初始化后创建的新地图中的关键帧。通过结果图观察, 融合后的地图与原始未丢失的结果对比差异不大。

## Slide 13
Map accuracy analysis
(c) Sequence MH_01_easy track comparison result
(b) Sequence V2_01_easy track comparison result
Convergence map and ground truth track comparison results
(a) Sequence V1_01_easy track comparison chart
Notes: Further, we can observe the trajectory of the camera and verify the accuracy of the fused map. The blue is the ground truth track. Red is the trajectory that the artificial manufacturing track loses and then fuses. It can be seen that the trajectory deviation is not large
进一步，我们可以观察相机的轨迹，验证融合地图的精确性。其中蓝色是ground truth轨迹。红色是人为制造跟踪丢失，然后融合得到的轨迹。可以看出来轨迹偏差不大。

## Slide 14
data set | scale | Root mean square error(/m) | average error(/m) | Median error(/m) | Standard variance(/m) | Minimum error(/m) | Maximum error(/m)
V1_01_easy | 0.998 | 0.092 | 0.089 | 0.089 | 0.024 | 0.015 | 0.149
V2_01_easy | 0.987 | 0.060 | 0.055 | 0.056 | 0.023 | 0.011 | 0.105
MH_01_easy | 1.017 | 0.073 | 0.069 | 0.066 | 0.023 | 0.021 | 0.136
V2_02_medium | 1.024 | 0.082 | 0.852 | 0.733 | 0.035 | 0.030 | 0.154
Global pose error comparison between fusion map and ground truth
Map accuracy analysis
Notes: This table gives a quantitative comparison. Our fusion method has a small variation, and the average difference from the real data does not exceed 10 centimeters.
这个表给出了quantitive 比较，我们的融合方法偏差比较小，和真实数据之间平均偏差不超过10cm。

## Slide 15
(a) ORB_SLAM and ground truth track comparison results
ORB_SLAM and map integrity comparison results of the algorithm
Map integrity analysis
(b) Comparison of the algorithm and ground truth track
Notes: On data V1_02_meduim, tracking failures occur without data processing. (a) In the figure on the left, this is the results of ORB_SLAM running on data V1_02_meduim are compared with those of ground truth, (b) In the figure on the right, The results of our algorithm running on data V1_02_meduim are compared with those of ground truth, and the part circled by yellow box is the missing part of the track obtained by ORB_SLAM algorithm. The part circled by the green box is the missing part of the algorithm trajectory. By comparing the two, we can see clearly that our algorithm has fewer missing parts and saves more complete maps.
在数据V1_02_meduim上，不需要经过数据处理也会出现跟踪失败的情况。(a)为ORB_SLAM在数据V1_02_meduim上的运行结果与ground truth的轨迹对比结果， (b)为我们算法在数据V1_02_meduim上运行结果与ground truth的轨迹对比结果，其中黄色方框圈出的部分为ORB_SLAM算法得到的轨迹所缺失的部分。绿色方框所圈出的部分为本文算法轨迹所缺失的部分。通过两者对比可以很清楚的看出，我们算法缺失部分更少，保存的地图更为完整。

## Slide 16
Ｒecovery of lost map for monocular simultaneous localization and mapping
Zhang J H， Wang Y Y， Wang Z Y， Chen S Y， Guan Q． Ｒecovery of lost map for monocular simultaneous localization and mapping［J］ ． Journal of Image and Graphics， 2018， 23( 3) :0372-0383．［张剑华，王燕燕，王曾媛，陈胜勇，管秋． 单目同时定位与建图中的地图恢复融合技术 ［ J］ ． 中国图象图形学报， 2018， 23( 3) :0372-0383．］［DOI:10. 11834/jig. 170505］
paper
references
Notes: We now certify that we refer to the paper published in the Chinese Journal of Image and Graphics in 2018 on the recovery of the lost map for monocular simultaneous localization and mapping.
特在此说明，我们参考的是2018年发表在中国图象图形学报上的单目同时定位与建图中的地图恢复融合这篇论文

## Slide 17
Thanks
data：2019.10.14
Respondent ： Ruyu Liu
Zhejiang University of Technology
浙江工业大学
Notes: Our report is over. Thanks.